## Slide 1
IRON &
STEEL
INDUSTRY
VALUE CHAIN
Maintenance Pain Points
& Strategic Levers
A comprehensive diagnostic across the full value chain — from raw material sourcing through iron-making, steel-making, rolling, and finishing — identifying critical failure modes and actionable maintenance strategies.
6
Stages
Value Chain
18+
Pain Points
Identified
30+
Levers
Solutions

## Slide 2
IRON & STEEL INDUSTRY — FULL VALUE CHAIN WITH MAINTENANCE PAIN POINTS & LEVERS
RAW MATERIAL
SOURCING
▶
IRON
MAKING
▶
STEEL
MAKING
▶
CASTING &
ROLLING
▶
FINISHING &
COATING
▶
DISTRIBUTION &
END PRODUCT
⚠ MAINTENANCE PAIN POINTS
✔ SOLUTION LEVERS
Supplier quality
variability
Moisture & grade
inconsistency
Stockpile contamination
& segregation loss
Supplier scorecards
& audits
Online moisture
analyzers
Automated stockyard
management
Blast furnace
lining wear
Bell & hopper
mechanism failure
Stove heat
exchanger fouling
Laser lining
profiling
Predictive vibration
monitoring
Online gas analysis
& CBM
BOF/EAF refractory
degradation
Electrode breakage
in EAF
Ladle lining
spalling
Thermal imaging
for refractory
AI-based electrode
optimizer
Ladle tracking
& heat logs
Mould oscillation
failure
Roll bearing
overheating
Scale buildup on
rolling stands
Mould lubrication
automation
Oil analysis
& CMS sensors
High-pressure
descaling systems
Coating thickness
non-uniformity
Annealing furnace
hot spots
Pickling tank
corrosion
Beta gauge
thickness control
Zone temp control
& profiling
Cathodic protection
& lining renewal
Surface defects
at dispatch
Cold-chain handling
damage
Inventory tracking
gaps
AI visual inspection
(camera)
IoT handling
monitoring
RFID/ERP inventory
integration
⚠ Pain Points ✔ Solution Levers — Subsequent slides provide in-depth detail per stage

## Slide 3
STAGE 01
RAW MATERIAL SOURCING
Iron Ore · Coking Coal · Limestone · Scrap
Fe% Variability < ±0.5%
Moisture < 8%
Conveyor OEE > 92%
Sinter Plant Availability > 95%
PROCESS FLOW: Mining / Procurement → Beneficiation → Pelletizing/Sintering → Stockpiling → Quality Testing → Feed to Blast Furnace
⚠ MAINTENANCE PAIN POINTS
1. Supplier Quality Variability
Inconsistent Fe% in iron ore leads to fluctuating blast furnace performance, increased coke rate, and higher energy consumption.
2. Moisture & Grade Inconsistency
Excessive moisture causes BF disruptions; grade variation (SiO₂, Al₂O₃) requires constant slag chemistry adjustments.
3. Stockpile Contamination & Segregation
Mixed-grade ore in stockpiles causes irregular sinter composition; dust and contamination degrade downstream quality.
4. Unplanned Equipment Downtime
Conveyors, stackers, reclaimers break down without warning. Single conveyor failure can halt entire raw material flow.
5. Sinter Plant Refractory Failures
Sintering strand and cooler refractories degrade rapidly, causing thermal inefficiency and unplanned shutdowns.
✔ SOLUTION LEVERS & MAINTENANCE STRATEGIES
1. Supplier Scorecards & Audit Programs
Establish chemistry acceptance bands; use vendor KPIs and spot sampling to enforce quality SLAs before shipment.
2. Online Moisture Analyzers (Microwave/NIR)
Real-time moisture measurement on conveyors enables automatic blend corrections and prevents BF disruptions.
3. Automated Stockyard Management Systems
GPS-tracked stackers/reclaimers with material database prevent grade mixing; optimize blending ratios dynamically.
4. Predictive Maintenance on Conveyors
Vibration sensors on bearings + thermal imaging on motors reduce MTTR by 40-60%; belt tear detection systems prevent catastrophic failures.
5. Digital Refractory Health Monitoring
Thermal cameras and periodic profile surveys on sinter strands predict lining life; schedule planned shutdowns instead of reactive repairs.
Iron & Steel Industry Value Chain — Stage 01: RAW MATERIAL SOURCING

## Slide 4
STAGE 02
IRON MAKING
Blast Furnace · Hot Stoves · Cast House · Torpedo Cars
BF Campaign Life > 15 years
Coke Rate < 380 kg/THM
Blast Temp > 1200°C
Tuyere Burnout Rate < 2/year
PROCESS FLOW: Burden Charging → Blast Furnace Smelting (1550°C) → Hot Metal Tapping → Slag Granulation → Torpedo Car Transport
⚠ MAINTENANCE PAIN POINTS
1. Blast Furnace Lining Wear & Erosion
Skull buildup and carbon block erosion in BF hearth — the costliest failure mode. Unplanned relines cause 45-90 day outages worth $50-150M losses.
2. Bell & Hopper / Bell-less Top Failure
Charging equipment failures disrupt burden distribution, causing channeling, poor gas utilization, and thermal imbalances.
3. Hot Stove Heat Exchanger Fouling
Dust and alkali deposit accumulation in stove checkers reduces blast temperature efficiency, increasing coke consumption.
4. Tuyere & Blowpipe Burnouts
Tuyere copper block failures from local hot spots cause emergency shutdowns; average 4-6 tuyere changes/year per furnace.
5. Torpedo Car Refractory Degradation
Torpedo ladle linings crack and spall due to thermal cycling; hot metal temperature drops during transport affecting steelmaking quality.
✔ SOLUTION LEVERS & MAINTENANCE STRATEGIES
1. BF Hearth Monitoring System (ABHMS)
Thermocouple arrays + skull modeling software provide real-time lining thickness estimates; early warning extends campaign life by 2-3 years.
2. Laser Profiling for Lining Wear
3D laser scanning during planned shutdowns maps wear patterns with ±2mm accuracy; enables targeted gunning and grouting campaigns.
3. Burden Distribution Optimization
Radar + X-ray burden profile sensors with AI-based distribution control improve gas utilization and reduce coke rate by 3-5%.
4. Online Gas Analysis & CBM on Stoves
Continuous CO/CO₂/H₂ measurement + infrared thermography on stoves enables condition-based maintenance; prevents costly checker damage.
5. Tuyere Cooling Water Monitoring
Flow + temperature sensors on each tuyere cooling circuit give 15-30 min warning before burnout; enables planned replacement vs. emergency stop.
Iron & Steel Industry Value Chain — Stage 02: IRON MAKING

## Slide 5
STAGE 03
STEEL MAKING
BOF / EAF → Ladle Metallurgy → Degassing
Refractory Life > 250 heats (BOF)
Electrode Consumption < 1.5 kg/t
Ladle MTBF > 50 heats
Heat-to-Heat Time < 40 min
PROCESS FLOW: Hot Metal Pretreatment → BOF/EAF Converter → Tapping → Ladle Furnace Refining → Vacuum Degassing → Alloy Addition → Transfer to Caster
⚠ MAINTENANCE PAIN POINTS
1. BOF/EAF Refractory Degradation
Converter vessel lining erodes 1-3mm per heat in high-wear zones (trunnion, charging side). Unplanned relines cost $2-5M in lost production.
2. EAF Electrode Breakage
Graphite electrode breakage during operation causes immediate melt disruption; replacing mid-heat costs 2-4 hours of production time.
3. Ladle Lining Spalling & Failure
Thermal shock causes ladle lining spalls; worst case is a ladle breakout — catastrophic safety incident with $10M+ cleanup costs.
4. Oxygen Blow Lance Failures
Lance tip burnout or skull buildup interrupts blow control, causing inconsistent carbon and heat chemistry.
5. Vacuum Degasser Vessel Integrity
RH degasser vessel skulling and snorkel wear reduces degassing efficiency; affects ultra-low carbon steel quality targets.
✔ SOLUTION LEVERS & MAINTENANCE STRATEGIES
1. Thermal Imaging for Refractory Life Prediction
IR cameras on BOF outer shell detect hot spots indicating lining wear; heat-by-heat tracking enables planned relines with 10-15 heat buffer.
2. AI-Based Electrode Consumption Optimizer
Machine learning models predict electrode length and regulate immersion depth; reduces electrode consumption by 8-12% and breakage events.
3. Ladle Tracking & Heat Logging System
RFID-tagged ladles with thermal history logs prevent reuse of at-risk ladles; slag detection sensor at tapping prevents carry-over.
4. Dynamic BOF Lance Control
Sublance measurements + dynamic blow models adjust lance height and oxygen flow in real-time; hits target [C] within ±0.005% consistently.
5. RH Vessel Skull Management
Scheduled oxygen lancing campaigns clear skull buildup; vessel lining profiling during turnarounds with planned gunning prevents campaign failures.
Iron & Steel Industry Value Chain — Stage 03: STEEL MAKING

## Slide 6
STAGE 04
CASTING & ROLLING
Continuous Caster → Hot Rolling Mill → Coiler
Breakout Rate < 0.05/month
Roll Change MTTR < 2 hrs
Surface Defect Rate < 0.5%
Reheating Furnace Efficiency > 82%
PROCESS FLOW: Tundish → Continuous Casting Mould → Strand Solidification → Slab/Billet Cutting → Reheating Furnace → Roughing Mill → Finishing Mill → Laminar Cooling → Coiling
⚠ MAINTENANCE PAIN POINTS
1. Mould Oscillation Mechanism Failure
Hydraulic oscillation system failures cause strand sticking, breakouts, and surface cracks. Breakout events cause 8-24 hour cleanup shutdowns.
2. Roll Bearing Overheating in Rolling Mills
High-speed roll bearings fail from inadequate lubrication or contamination; unplanned roll change causes 4-8 hours of downtime per event.
3. Scale Buildup on Rolling Stands
Iron oxide scale embedded into strip surface causes surface defect rejection rates of 2-5%; damages roll surfaces prematurely.
4. Reheating Furnace Burner & Skid Failures
Burner failures create temperature non-uniformity in slabs (skid marks); leads to thickness variation and strip shape defects in rolling.
5. Coiler Mandrel & Wrapper Roll Wear
Mandrel and wrapper roll wear causes coil telescoping and loose-wrap defects; increases customer rejection rate.
✔ SOLUTION LEVERS & MAINTENANCE STRATEGIES
1. Mould Breakout Detection System (BODS)
Thermocouple matrices in mould + AI pattern recognition provide 30-90 second breakout warning; auto-triggers casting speed reduction and alarm.
2. Automated Roll Shop with CBM
Acoustic emission + vibration monitoring on roll bearings; roll surface inspection with profilometer; planned roll change scheduling.
3. High-Pressure Descaling System Optimization
Automated high-pressure descaling (200-400 bar) with pressure profiling eliminates surface scale; AI-controlled spray patterns reduce water usage 15%.
4. Reheating Furnace Digital Twin
Model-based temperature control + furnace digital twin optimizes heating curves; reduces fuel consumption 5-8% and eliminates skid mark defects.
5. Strip Shape & Profile Closed-Loop Control
X-ray thickness gauge + flatness meter feedback to rolling mill actuators (CVC, WRB); maintains ±0.3% thickness tolerance consistently.
Iron & Steel Industry Value Chain — Stage 04: CASTING & ROLLING

## Slide 7
STAGE 05
FINISHING & COATING
Pickling · Cold Rolling · Annealing · Galvanizing · Temper Mill
Coating Weight CV < 3%
Tube Failure Rate < 2/year
Acid Loss < 12 kg/t
HDG Dross < 0.8% of zinc consumption
PROCESS FLOW: Hot-rolled Coil → Pickling Line → Cold Rolling Mill → Bell/CAL Annealing → Hot-dip Galvanizing (HDG) → Temper Mill → Inspection → Slitting/Cutting → Shipping
⚠ MAINTENANCE PAIN POINTS
1. Coating Thickness Non-Uniformity
Zinc coating weight variation beyond ±5 g/m² causes customer rejections in automotive and appliance segments; difficult to detect post-line.
2. Annealing Furnace Hot Spots & Tube Failures
Radiant tubes in bell furnaces crack from thermal cycling; localized hot spots cause overannealing, softness variation, and surface oxidation.
3. Pickling Tank Corrosion & Acid Leaks
HCl pickling tanks develop leaks from corrosion; acid fumes damage nearby equipment; unplanned shutdowns for repair cause schedule disruption.
4. Cold Mill Roll Force Asymmetry
Chattermarks and edge waviness from roll force imbalance; worn backup roll bearings cause vibration patterns transferred to strip surface.
5. Snout & Pot Zinc Quality Degradation
Dross formation in galvanizing pot increases zinc consumption 8-12%; pot temperature non-uniformity creates coating adhesion failures.
✔ SOLUTION LEVERS & MAINTENANCE STRATEGIES
1. Beta Gauge / X-ray Coating Thickness Control
Closed-loop coating weight control via beta/X-ray gauge feedback to air knife gap; achieves ±2 g/m² consistency across full strip width.
2. Radiant Tube Condition Monitoring
Continuous tube temperature scanning + dew point monitoring; planned tube replacement schedules prevent in-furnace failures and strip contamination.
3. Acid Concentration Control & Tank Lining Renewal
Automatic HCl concentration control with dosing systems; FRP-lined tanks + periodic thickness inspection schedule prevents leaks.
4. Chatter Detection & Roll Grinding Optimization
Vibration analysis on mill stands detects chatter modes; off-line roll grinder with automated SFC profile inspection optimizes grinding cycles.
5. Galvanizing Pot Digital Management
Zinc pot composition control (Al, Fe content) + bath temperature uniformity via immersion stirrers; dross removal robot reduces zinc loss 10%.
Iron & Steel Industry Value Chain — Stage 05: FINISHING & COATING

## Slide 8
STAGE 06
DISTRIBUTION & END PRODUCT
Inspection · Warehousing · Logistics · Customer Delivery
Dispatch Defect Rate < 0.2%
Transit Damage < 0.1%
Traceability Coverage 100%
Customer Claim Resolution < 5 days
PROCESS FLOW: Final Quality Inspection → Weighing & Marking → Warehouse Storage → Order Picking → Loading (Road/Rail/Sea) → Customer Delivery → Claims Management
⚠ MAINTENANCE PAIN POINTS
1. Surface Defects Detected at Dispatch
Late detection of coil-end defects, edge cracks, or surface inclusions causes costly rework or downgrade; average defect detection cost 5x higher at dispatch vs. in-process.
2. Handling Damage During Loading/Transit
Coil edge denting from improper crane handling or poor saddle design; inadequate strapping causes coil unwinding in transit.
3. Inventory Tracking & Traceability Gaps
Manual labeling errors cause shipment of wrong grade; heat/batch traceability gaps create compliance risk for certified steel applications.
4. Corrosion During Storage
Inadequate storage conditions (humidity, condensation) cause rust staining within 30-60 days; especially critical for cold-rolled and CRCA products.
5. Customer Claims & Warranty Management
Without proper heat-level data, root cause analysis of customer claims takes weeks; poor data causes unjustified warranty costs.
✔ SOLUTION LEVERS & MAINTENANCE STRATEGIES
1. AI-Powered Visual Inspection Systems
Surface inspection cameras with deep learning models detect surface defects at line speed (>200 m/min); automatic downgrade/rejection reduces dispatch rejections 70%.
2. Coil Handling Best Practices & IoT Monitoring
Calibrated C-hooks with load cells; coil saddle IoT sensors detect improper stacking; automated coil car systems eliminate manual crane errors.
3. RFID + ERP Full Traceability Platform
RFID tags on every coil/slab linked to heat records in ERP; full genealogy from raw material to customer enables instant recall and certification.
4. Climate-Controlled Storage & VCI Packaging
Volatile Corrosion Inhibitor (VCI) packaging for sensitive products; humidity monitoring in warehouse; FIFO inventory rotation with automated planning.
5. Digital Customer Claims Analytics
Defect image database linked to process parameters enables rapid root cause analysis; trend analytics reduce repeat defect occurrences by 40-60%.
Iron & Steel Industry Value Chain — Stage 06: DISTRIBUTION & END PRODUCT

## Slide 9
CROSS-CUTTING MAINTENANCE LEVERS — STRATEGIC SUMMARY
PREDICTIVE
MAINTENANCE
▸ Vibration, thermal & acoustic monitoring on all critical rotating equipment
▸ Machine learning models for failure prediction with 2-4 week horizon
▸ Integration with CMMS for auto-generated work orders
▸ Reduces unplanned downtime 35-50%
DIGITAL TWIN
& SIMULATION
▸ BF hearth, rolling mill, and reheating furnace digital twins
▸ Real-time process state estimation from sensor fusion
▸ What-if analysis for campaign life extension decisions
▸ Reduces reline frequency by 10-20%
REFRACTORY
LIFECYCLE MGT
▸ 3D laser scanning at every turnaround for wear mapping
▸ Heat-by-heat refractory consumption tracking
▸ Planned gunning/shotcreting campaigns between relines
▸ Extends converter campaign life by 15-25%
QUALITY
INTELLIGENCE
▸ In-line sensors replace end-of-line quality checks
▸ Statistical Process Control on all key parameters
▸ AI visual inspection for 100% surface coverage
▸ Reduces quality-related losses by 40-60%
ENERGY &
UTILITY MGMT
▸ Energy management system across all utilities
▸ Gas network optimization (BFG/COG/steam balance)
▸ Compressed air leak detection with ultrasonic sensors
▸ Energy savings 5-10% from systematic management
WORKFORCE &
KNOWLEDGE
▸ Operator digital checklists replace paper round-sheets
▸ AR/VR-assisted maintenance procedures for complex tasks
▸ Knowledge capture from retiring craftsmen into AI systems
▸ Reduces craft error-related incidents by 60%
Building a Zero-Unplanned-Downtime Steel Plant requires simultaneous investment in technology, process discipline, and people capability.