## Slide 1
PELLET
IQ
AI Transformation Dashboard
PLANT
ArcelorMittal Nippon Steel India
LOCATION
Visakhapatnam (Vizag)
CAPACITY
8 MTPA — Straight Grate
FOCUS
Iron Ore Pelletizing
₹57 Cr/yr
Fuel Optimization
₹36 Cr/yr
Quality Prediction
₹17 Cr/yr
Moisture Control AI
₹11 Cr/yr
Stacker Reclaimer Opt.
TOTAL AI VALUE POTENTIAL
₹ 112 – 154 Crore / Year
8 MTPA basis · Conservative estimate · All use cases
PRIORITY USE CASES — DEEP DIVES IN THIS DECK
① Induration Furnace Fuel Optimization — PINN + MPC
② Pellet Quality Prediction — Ensemble ML (RF + XGBoost + LSTM)
③ Slurry & Filtration Moisture Control — XGBoost + LSTM
④ Stacker / Reclaimer Blend Optimization — Reinforcement Learning
CONFIDENTIAL — Prepared by Capgemini Engineering & AI Practice · AM/NS Vizag · 2025

## Slide 2
PRESENTATION STRUCTURE
End-to-End AI Transformation · 4 Priority Use Cases · Sensor Architecture · Industrial Benchmarking
01
Process Overview
AM/NS Vizag 8 MTPA Pellet Plant — Straight Grate
02
Use Case: Fuel Optimization
Induration Furnace · PINN + MPC · Sensor Architecture · Data Flow
03
Use Case: Quality Prediction
Pellet CCS/TI/AI · Ensemble ML · Soft Sensors · Data Flow
04
Use Case: Moisture Control AI
Slurry & Filtration · XGBoost+LSTM · Sensors · Data Flow
05
Use Case: Stacker Reclaimer
Blend Optimization · RL Agent · Sensors · Data Flow
06
Sensor Deep Dive & Comparison
All Sensors Analysed · Comparative Table · Preferred Recommendation
07
Peer Industry Reference
Which Sensor Used Where · Steel / Mining / Cement / Chemical
08
Business Value & Roadmap
Financial Impact · Implementation Timeline · Next Steps
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 3
AM/NS VIZAG — 8 MTPA STRAIGHT GRATE PELLET PLANT
Process Flow Overview · Key Parameters · AI Intervention Points
RAW MATERIAL YARD
Iron Ore Fines
63.2% Fe · 9.8% moisture
1,120 t/h
GRINDING
Ball Mill Circuit
Blaine 1650-1750 cm²/g
1,092 t/h
FILTRATION
Vacuum Disc Filters
Moisture 8.6-9.1%
1,045 t/h
BALLING
Disc Pelletizers
Green Ball D50 12mm
1,028 t/h
INDURATION
Straight Grate Furnace
1,280°C peak · 55 Mcal/t tgt
1,002 t/h
SCREENING
Vibrating Screens
8-16mm product cut
964 t/h
⚡ ④ SR-AI
⚡ ③ Moisture AI
⚡ Disc APC
⚡ ① Furnace AI
② PELLET QUALITY PREDICTION AI — monitors & predicts across all stages (Green Ball → Indurated Pellet → Lab Result)
Specific Fuel
62.4
→ 55.0
Mcal/t
TARGET
CCS
234
→ 258
daN/p
TARGET
Tumble Index
93.8
→ 95.5
%
TARGET
On-Size Yield
86.4
→ 89.8
%
TARGET
Availability
94.2
→ 95.5
%
TARGET
Moisture (FC)
9.1
→ 8.6
%
TARGET
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 4
① INDURATION FURNACE FUEL OPTIMIZATION
Physics-Informed Neural Network (PINN) + Model Predictive Control · End-to-End Data Flow
AM/NS VIZAG · 8 MTPA
1
RAW INPUTS
Green ball properties
Moisture, size, drop strength
Ore chemistry, bentonite %
2
SENSOR LAYER
Thermocouples, O2/CO2 analyser
Gas flow meters, pressure xmtrs
Waste gas composition
3
DCS / SCADA
Siemens PCS7 / OSIsoft PI
Tag capture @1-5s interval
20,000+ tags ingested
4
FEATURE ENG.
Zone temp profiles
Gas stoichiometry calc
Feed rate normalization
5
PINN MODEL
Combustion physics
embedded in NN layers
Zone-wise inference
6
MPC CONTROL
Optimal setpoints
Fan speed, fuel valves
Zone-wise dispatch
7
OUTPUT / KPIs
Specific fuel 55 Mcal/t
CCS 258 daN/p
₹57 Cr/yr saving
🧠 AI ENGINE — PINN + MPC — FURNACE COMBUSTION OPTIMIZATION
Physics-Informed NN
Combustion kinetics (Arrhenius), heat transfer coefficients and thermodynamic constraints embedded as physics loss terms. Trained on 4-yr operational data. Zero extrapolation risk beyond physics limits.
Feature Store (real-time)
Green ball properties (moisture, size, drop #), ore chemistry (FeO, SiO2, CaO), atmospheric humidity, ambient temp, previous-zone fuel actuals — 180+ features updated every 30s.
MPC Controller
PINN provides forward simulation of furnace state; MPC optimizes 6-zone fuel setpoints to minimize total Mcal/t while maintaining CCS≥255 and TI≥95. Constraint-aware, DCS-integrated.
Explainability (SHAP)
Top 5 drivers displayed for operator on each decision: zone temp deviation, green ball moisture, O2 excess, FeO level, draft pressure. Ensures operator trust and acceptance.
KEY SENSORS
Thermocouple (K/R-type)
Temperature · Multiple Zones
8-12 thermocouples per zone. K-type up to 1200°C; R-type (Pt/Rh) for 1300°C+ zones. Redundant pairs critical. ±0.75% accuracy.
O2/CO2 In-Situ Analyser
Combustion Gas · Zirconia cell
Zirconia-based electrochemical O2 sensor + NDIR CO2. Positioned in waste gas ducts. Response time <5s. Required for stoichiometric control.
Gas Flow Meter
Coriolis / Thermal Mass
Fuel gas and combustion air flow. Coriolis preferred for accuracy (±0.2%); thermal mass for air ducts. Critical for Mcal/t calculation.
Draft Pressure Sensor
Differential Pressure
Wind box to plenum chamber ΔP. Capacitive or piezo DP transmitters. Controls gas throughput per zone. Range 0-1500 Pa.
Waste Gas Pyrometer
Radiation Thermometer
Non-contact IR for pellet bed surface temp at discharge end. Complements thermocouple reading. ±5°C accuracy at 900-1100°C.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 5
② PELLET QUALITY PREDICTION — CCS / TUMBLE / ABRASION INDEX
Ensemble ML: Random Forest + XGBoost + LSTM · 45-min Ahead Prediction · SHAP Explainability
AM/NS VIZAG · 8 MTPA
1
GREEN BALL DATA
D50, D10/D90, moisture
Drop test strength
Disc throughput
2
PROCESS DATA
Zone temps (8 zones)
Fuel/air ratios
Bed thickness, speed
3
ORE CHEMISTRY
FeO, SiO2, CaO, Al2O3
LOI, moisture batch
Blaine surface area
4
FEATURE MERGE
Time-lag alignment
(45-min delay)
Smoothing + imputation
5
ENSEMBLE ML
RF + XGBoost base
LSTM time sequence
Stacked meta-learner
6
QUALITY FORECAST
CCS, TI, AI predicted
45-min before lab
Confidence interval
7
ACTION / ALERT
Setpoint adjustment
Lab pre-alert
Rejection prevention
🧠 AI ENGINE — ENSEMBLE MODEL — CCS / TUMBLE INDEX / ABRASION INDEX
Random Forest (Base)
500 trees, max-depth 12. Input: 80+ process/chemistry features. Captures non-linear interactions. SHAP values computed per prediction for operator explanation. Robust to noisy sensor data.
XGBoost (Base)
Gradient boosted trees; captures sharp transitions during blend changes or feed disruptions. Optimized for RMSE of CCS (±8 daN/p target). L1/L2 regularization to prevent overfit on chemistry changes.
LSTM (Sequence Model)
60-step (30-min) lookback on zone temperature trajectories, fuel flow history. Captures temporal patterns in induration profile evolution. Hidden dim 128, 2 layers, dropout 0.2.
Stacked Meta-Learner
Ridge regression meta-model combines RF + XGB + LSTM predictions. Output: CCS (target ≤±12 daN/p error), TI (±1.5%), AI (±0.3%). Prediction issued every 2 min with 45-min horizon.
KEY SENSORS
Green Ball Drop Tester
Mechanical · Automated
Automated drum-drop tester on disc discharge belt. Samples every 15 min. Drop number >6 = good forming. Direct predictor for final CCS.
Laser PSD Analyser
Laser Diffraction · Online
CILAS or Malvern online PSD on green ball stream. D50, D10, D90 measured in real-time. Belt-mounted or slipstream. Critical for size dist. model input.
NIR Moisture Sensor
Near-Infrared · Non-contact
On-belt NIR for green ball moisture before disc feed. Accuracy ±0.3%. Hydronix or Berthold preferred. Direct feed into LSTM sequence model.
Thermocouple Array (PDHC)
K/S-type · Zone mapped
Pre-heat, drying, firing, and cooling zone temps. Maps the full thermal history which is the dominant predictor of CCS. Redundant pairs per zone.
XRF Analyser (Online)
X-Ray Fluorescence · Belt
Online XRF on ore blend or slurry for FeO, SiO2, CaO, MgO. Thermo Fisher or Bruker. Updates chemistry features every 30s. Critical for flux ratio.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 6
③ SLURRY & FILTRATION MOISTURE CONTROL AI
XGBoost + LSTM Hybrid · 15-min Ahead Moisture Prediction · Vacuum & Flocculant Prescriptions
AM/NS VIZAG · 8 MTPA
1
ORE SLURRY
Slurry density & flow
Solid content 35%
Particle PSD (Blaine)
2
FILTER FEEDS
Vacuum disc filter
Feed box level
Flocculant dosing rate
3
SENSOR INPUTS
Microwave moisture
Load cell (cake weight)
Vacuum pressure ΔP
4
DATA PIPELINE
OSIsoft PI Connector
1-sec resolution
Quality validation
5
XGBOOST + LSTM
15-min ahead forecast
Moisture deviation alert
±0.15% target accuracy
6
PRESCRIPTIONS
Vacuum pressure cmd
Flocculant dose adjust
Feed rate modulate
7
DOWNSTREAM KPIs
FC Moisture 8.6%
CCS +6 daN/p indirect
₹17 Cr/yr impact
🧠 AI ENGINE — XGBOOST + LSTM HYBRID — FILTER CAKE MOISTURE PREDICTION
XGBoost — Static Features
Ore mineralogy (hardness, porosity), flocculant type and dosing rate, feed slurry solid %, filter disc RPM, number of active filter segments. Captures process setpoint relationships.
LSTM — Dynamic Sequence
60-step (15-min) history of vacuum pressure, cake thickness (load cell), feed box level, and production rate. LSTM captures lag between vacuum adjustment and moisture response (8-12 min typical).
Ensemble Combiner
XGBoost prediction (static) + LSTM prediction (dynamic) combined via weighted average (0.35 / 0.65). Weights re-optimized weekly via rolling validation. Target: MAE < 0.15% moisture.
Prescriptive Actions
If predicted moisture > 9.0%: increase vacuum by +50 mbar, reduce feed rate by 5%. If predicted moisture < 8.3%: reduce vacuum by 30 mbar to save energy. Flocculant dose adjusted proportionally.
KEY SENSORS
Microwave Moisture Sensor
Microwave Transmission
On-belt or in-chute. Berthold Gravimat or Vega. Penetrates bulk cake, ±0.2% accuracy. No contact — no wear. Update rate 1-2s. Primary moisture feedback.
Load Cell (Belt Weigher)
Strain Gauge · Belt-mounted
Continuous cake throughput measurement. Combined with moisture to give water tonnage/hr. Calibration monthly. Accuracy ±0.5% of full scale.
Vacuum Pressure Transmitter
Differential Pressure · Piezo
Filter drum to vacuum receiver ΔP. 0-1 bar range. Capacitive DP or piezo. Key control variable — direct influence on moisture. Response <1s.
Density Meter (Slurry)
Nuclear / Coriolis
Radiometric (Berthold) or Coriolis (Endress+Hauser) for slurry density at filter feed. Solid content calculation feed input to model. ±0.5 kg/L accuracy.
NIR Moisture (Discharge)
Near-Infrared · In-line
Final cake moisture validation at discharge conveyor. Hydronix HDi or Berthold LB 475. Closes the feedback loop between prediction and reality.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 7
④ STACKER / RECLAIMER BLEND OPTIMIZATION — RL AGENT
Proximal Policy Optimization (PPO) · Fe Grade Homogeneity · Real-Time Blend Control
AM/NS VIZAG · 8 MTPA
1
ORE RECEIPT
Vessel/rake unloading
Multiple ore types (4-6)
Chemistry certificates
2
YARD MAPPING
GPS + LIDAR 3D scan
Stock pile inventory
Layer chemistry model
3
BLEND TARGET
Target Fe 63.5%
Moisture ≤9.5%
Silica ≤3.5%
4
RL OBSERVATION
Current pile chemistry
Reclaim queue position
Production demand
5
PPO AGENT
Action: SR sequence
Reward: blend deviation
Penalty: switch cost
6
SR DISPATCH
SR-1 / SR-2 commands
Bucket wheel RPM
Travel speed
7
BLEND OUTCOME
Fe σ < 0.19%
Moisture variation ↓46%
₹11 Cr/yr impact
🧠 AI ENGINE — PROXIMAL POLICY OPTIMIZATION (PPO) — STACKER/RECLAIMER SEQUENCING
State Space
Current stockpile chemistry (Fe, SiO2, Al2O3, moisture) per layer/pile, SR-1 and SR-2 positions, production rate demand, reclaim queue length, ship unloading status. ~120-dim state vector.
Action Space
Select which pile to reclaim next, set reclaim rate (t/h), set travel speed, activate/deactivate SR. Continuous action space for rate; discrete for pile selection. Multi-agent for SR-1 + SR-2.
Reward Function
Primary reward: −|blend_Fe − 63.5%| − 0.5×|blend_SiO2 − 3.2%|. Penalty: −0.2 per SR switch (energy cost). Bonus: +1.0 if running at target throughput. Discount factor γ=0.99.
Training / Deployment
PPO trained in simulation (digital twin of ore yard). 10M simulation steps before live deployment. Shadow mode for 4 weeks before control handover. Online learning with daily reward updates.
KEY SENSORS
3D LIDAR Scanner
Time-of-Flight · Yard-wide
Sick LMS or Leica 3D scanner mounted on gantry. 360° coverage. Point cloud → stockpile volume + height map. Updates every 30 min. ±5 cm accuracy.
Online XRF (Reclaim Belt)
X-Ray Fluorescence · Real-time
Thermo Fisher or Bruker on reclaim belt conveyor. Fe, SiO2, Al2O3, CaO, P, S measured every 30s. Forms real-time blend feedback to RL agent.
Microwave Moisture (Belt)
Microwave Transmission
On reclaim belt conveyor. Moisture of reclaimed ore before grinding. Berthold or Vega. Updates blending model with actual moisture, not certificate.
Belt Weigher (Reclaim)
Load Cell · Continuous
Tonnes per hour on reclaim belt. Combined with XRF chemistry to give instantaneous blend composition. Accuracy ±0.5% of reading.
GPS / Encoder (SR Position)
RTK-GPS + Rotary Encoder
Real-time SR boom position and travel distance. Sub-meter accuracy. Combined with LIDAR height map to identify reclaim zone chemistry per layer.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 8
SENSOR DEEP DIVE — TEMPERATURE & COMBUSTION SENSORS
Induration Furnace · Comparative Analysis · Preferred Recommendation · Peer Reference
Sensor Type
Range
Accuracy
Response
Cost
Durability
AM/NS Vizag Recommendation
Type K Thermocouple
(NiCr/NiAl)
−200 to 1260°C
±0.75%
1-3s
Low
3-6 mo
✓ Primary for zones 1-5 (up to 1200°C). Cost-effective, DCS-native. Replace every 3 months.
Type R Thermocouple
(Pt13%Rh/Pt)
0 to 1600°C
±0.25%
2-4s
High
12 mo
✓✓ PREFERRED for firing zone (1250-1350°C). Platinum alloy — superior accuracy, longer life.
Type S Thermocouple
(Pt10%Rh/Pt)
0 to 1600°C
±0.25%
2-4s
High
12 mo
✓ Alternative to R-type. Used where Type S calibration preferred. Similar performance.
Radiation Pyrometer
(IR Non-contact)
600 to 1800°C
±5°C
<100ms
Med-High
5+ yr
✓ Recommended for pellet bed surface at soaking/cooling transition. No drift, no replacement.
Optical Pyrometer
(2-color)
700 to 2000°C
±0.5%
<50ms
High
5+ yr
Suitable for very high-temp measurement. Emissivity-independent. Consider for critical firing zone.
Thermowell + RTD
(Pt100)
−50 to 800°C
±0.1°C
5-15s
Med
2+ yr
Use for cooler section and gas header temp where precision needed but temp <800°C.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 9
SENSOR DEEP DIVE — MOISTURE, COMPOSITION & PARTICLE SIZE
Filtration · Balling · Grinding Circuits · Recommended Technology vs Alternatives · Peer Industry
Sensor Type
Technology
Accuracy
Update
Cost
Maintenance
Recommendation & Preferred Make
Microwave Moisture
On-Belt
Microwave transmission
±0.2%
1-2s
Med-High
Low
✓✓ PREFERRED. Berthold Gravimat or Vega VEGAWAVE 81. Penetrates bulk. Non-contact. Proven in iron ore filtration globally.
NIR Moisture Sensor
In-line / On-belt
Near-infrared reflectance
±0.3%
1s
Med
Low
✓ Good for surface moisture. Hydronix HDi or Berthold LB 475. Less accurate for thick cakes. Use as secondary/validation sensor.
Capacitance Moisture
(Probe)
Dielectric constant
±0.5%
0.5s
Low
Med
Secondary only. Prone to fouling in iron ore slurry. Requires calibration per ore type. Not recommended as primary.
Nuclear Density
(Slurry)
Gamma ray absorption
±0.5 kg/L
1s
High
Low
✓ Berthold LB 444 for slurry density. Requires radiation licence. Highest accuracy. Used by most major iron ore plants.
Online XRF Analyser
(Belt / In-stream)
X-ray fluorescence
±0.1% Fe
30s
Very High
Med
✓✓ PREFERRED for chemistry. Thermo Fisher Metals Courier 7i or Bruker S2 KODIAK. 30s updates, multi-element.
Laser PSD Analyser
(Online)
Laser diffraction
D50 ±2%
15s
High
Med
✓ Malvern Insitec or CILAS for green ball PSD. Slipstream configuration. D50 accuracy ±2% of reading. Key for yield prediction.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 10
PEER INDUSTRY SENSOR REFERENCES
Which Sensor Technology is Used Where — Steel · Mining · Cement · Chemicals
Type R/S TC
(Hi-temp)
Microwave
Moisture
Online XRF
(Chemistry)
Laser PSD
(Particle)
Nuclear
Density
IR Pyrometer
(Non-contact)
Steel
(Pelletizing)
✓✓
✓✓
✓✓
✓✓
✓✓
✓✓
Iron Ore
(Mining)
✓
✓✓
✓✓
✓
✓✓
✓
Cement
(Kiln)
✓✓
✓✓
✓
✓✓
✓
✓✓
Chemical
(Reactors)
✓
✓
✓✓
✓
✓✓
✓
Power
(Boilers)
✓✓
○
○
○
✓
✓✓
✓✓ Primary / Proven at scale
✓ Used / Proven
○ Limited / Niche use
Iron Ore / Pelletizing
Microwave moisture (Berthold) and nuclear density standard on all major pellet plants (South American producers, Nordic iron ore miners). Online XRF on reclaim belt is now near-universal in greenfield plants post-2015.
Cement (Kiln)
Type S/R thermocouples with 6-month replacement cycle in preheater/kiln. Radiation pyrometers for clinker temp at kiln discharge. NIR moisture on raw meal — standard for 20+ years.
Chemical (Reactors)
Online XRF used extensively for catalyst quality and product composition monitoring. Nuclear density meters in slurry reactors. Coriolis flow meters preferred over magnetic for density measurement.
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 11
MASTER SENSOR RECOMMENDATION — AM/NS VIZAG
Consolidated Preferred Sensor List · All 4 Use Cases · Technology, Make, Location, Priority
Use Case
Parameter
Sensor Type
Preferred Make
Location
Priority
Qty
Fuel Opt.
Zone Temperature
Type R Thermocouple
Omega / Heraeus
8 zones × 3 ports
CRIT
24
Fuel Opt.
O2 / CO2 Combustion
Zirconia O2 + NDIR CO2
Siemens Ultramat
Waste gas ducts (6)
CRIT
6
Fuel Opt.
Fuel Gas Flow
Coriolis Flow Meter
Endress+Hauser
Fuel gas headers
HIGH
12
Fuel Opt.
Draft Pressure
DP Transmitter
Honeywell STD
Wind box / plenum
HIGH
24
Quality Pred.
Green Ball PSD
Laser Diffraction PSD
Malvern Insitec
Disc discharge belt
CRIT
4
Quality Pred.
Green Ball Moisture
NIR Moisture Sensor
Hydronix HDi
Pre-disc feed
HIGH
4
Quality Pred.
Ore Chemistry
Online XRF Analyser
Thermo Fisher MC7
Reclaim + filter feed
CRIT
2
Quality Pred.
Bed Surface Temp
Radiation Pyrometer
Land Cyclops
Post-firing / cooling
HIGH
3
Moisture AI
Filter Cake Moisture
Microwave Moisture
Berthold Gravimat
Filter discharge belt
CRIT
6
Moisture AI
Cake Weight / Throughput
Belt Weigher (LC)
Schenck Process
Filter discharge
HIGH
6
Moisture AI
Vacuum Pressure
DP Transmitter
Endress+Hauser
Filter drum–receiver
CRIT
12
Moisture AI
Slurry Density
Nuclear Density Meter
Berthold LB 444
Filter feed line
HIGH
3
SR Blend Opt.
Stockpile Volume
3D LIDAR Scanner
Sick LMS 511
Yard gantry (2 units)
HIGH
2
SR Blend Opt.
Reclaim Chemistry
Online XRF (Belt)
Thermo Fisher MC7
Reclaim belt
CRIT
1
SR Blend Opt.
Reclaim Moisture
Microwave Moisture
Berthold Gravimat
Reclaim belt
HIGH
1
CONFIDENTIAL · Capgemini Engineering & AI Practice · Total 133 sensor instruments across 4 AI use cases

## Slide 12
BUSINESS VALUE SUMMARY — ALL 4 USE CASES
8 MTPA · AM/NS Vizag · Annual Value Projection · Conservative Estimates
① Fuel Optimization
₹ 57.3 Cr
per year
11.9% fuel reduction
62.4→55.0 Mcal/t
② Quality Prediction
₹ 36.3 Cr
per year
+24 daN/p CCS
−60% rejections
③ Moisture Control AI
₹ 16.8 Cr
per year
−0.5% moisture dev.
+32 t/h yield
④ Stacker Reclaimer
₹ 11.2 Cr
per year
Fe σ 0.35→0.19%
−46% blend variance
TOTAL PROGRAMME VALUE
₹ 112 – 154 Crore / Year
3-year cumulative: ₹336 – 462 Cr · IRR >180% · Payback <8 months
Phase 1
(Q1–Q2)
Foundation
Data infrastructure
Sensor validation
Baseline AI models
Phase 2
(Q3–Q4)
Deploy Use Cases 1–2
Furnace AI + MPC live
Quality prediction live
Operator training
Phase 3
(Q5–Q6)
Deploy Use Cases 3–4
Moisture AI live
SR optimization live
Value measurement
Phase 4
(Q7+)
Scale & Optimise
Digital twin full
AI self-tuning
Expand to sinter
CONFIDENTIAL · Capgemini Engineering & AI Practice

## Slide 13
THE AI-POWERED PELLET PLANT
STARTS WITH THE RIGHT DATA, THE RIGHT SENSORS, AND THE RIGHT PARTNER
1
Sensor Audit & Gap Analysis
Validate existing sensor coverage vs recommended list. Identify gaps. Procurement & installation plan (est. 8-12 weeks).
2
Data Infrastructure Setup
OSIsoft PI / cloud historian. Data quality validation. Feature store setup. Baseline model training on 24 months historical data.
3
Proof of Concept — 90 Days
Deploy Furnace Fuel Optimization on 1 strand. Measure fuel saving. Demonstrate ₹10-15 Cr annualised impact. Greenlight for full rollout.
₹112–154 Crore per year · Payback in <8 months · IRR >180%
Conservative estimate · 8 MTPA basis · Capgemini will co-invest in PoC outcomes
CONFIDENTIAL — NOT FOR EXTERNAL DISTRIBUTION · Prepared by Capgemini Engineering & AI Practice · AM/NS Vizag · 2025